B1006-4P-65W

6 Ports 10/100M POE Switch

Product Description:

B1006-4P-65W is 6 ports 10/100M POE Switch. It provides 6 10/100Mbps Auto-Negotiation RJ45 ports and 4 ports with POE function (Port 2-5), the POE ports support full POE standard: IEEE802.3af and IEEE802.3at. The B1006-4P-65W is a small size metal-shell device which is useful for the small office, home and the IP solution project using. All POE ports support both IEEE802.3af and IEEE802.3at Standard; each port can output 30W max. This model has three optional power supplies for your choice (65W, 96W, 135W, can choose from the order list). Extend Function: Port Lightning protection, Power lightning protection.

Products Features:

- IEEE802.3, IEEE 802.3u, IEEE 802.3ab, IEEE802.3z, IEEE802.3af, IEEE802.3at

- Provides 6 10/100Base-TX ports

- 4 POE Ports (Ports 2-5), Each POE port output 30W max power

- High back-plane bandwidth 1Gbps

- Reliable Power Adapter supply power for both network switch and POE

- Three optional power adapters: 65W, 96W, 135W

- 1K entry MAC address table of the PoE switch with auto-learning and auto-aging

- IEEE802.3x Flow control for Full-duplex Mode and backpressure for Half-duplex Mode

- Surge protection for power port and data ports

- Supports PoE IEEE 802.3af or IEEE802.3at compliant Powered Device (PD)

- Compact metal case for desktop or wall-mounting.

- EMI standards complies with FCC, CE class B

Products Specifications:

| Item | Description |
| --- | --- |
| Summarize |
| Fixed port | 6 10/100Mbps RJ45 port |
| POE Port | 4 PoE ports (Port 2-5) |
| LED Indicators | PWR, PoE, Link/Act LED. |
| Input voltage | 100V～240V AC，50/60Hz (for power adapter) 48VDC (for switch) |
| Network Media | 10BASE-TX: UTP category 5, 5e cable (≤250m) 100BASE-TX: UTP category 5, 5e cable (≤150m) |
| Forwarding Rate | 10BASE-T: 14880pps/port 100BASE-TX: 148800pps/port |
| Power Supplies | 65W,96W,135W Optional |
| Operating temperature | 0℃～40℃. |
| Storage temperature | -10℃～70℃. |
| Relative humidity | 20%～85% (non-condensing). |
| Thermal methods | Fanless |
| Switching capacity | 1G. |
| MAC address table | 1K. |
| Traffic control | IEEE 802.3x full-duplex flow control. |
| Package Size | 19.1*14.1*6.4cm |
| Weight | <2Kg |
| Package | B1006-4P-65W POE switch User Manual Warranty Card Power Adapter Power Cable |
| PoE |
| PoE port | 6 10/100Base-TX ports. |
| PoE Standard | IEEE802.3af, IEEE802.3at, per port 15.4W,max 30W |
| Pin assignment | V+ (RJ45 Pin 3, 6), V- (RJ45 Pin 1, 2). |
| Extend Function | Port Lightning protection, Power lightning protection, solid vlan. |

Order Information

| B1006-4P-65W | 6 ports network Switch with 4 PoE Ports(Total Power 65W) |
| --- | --- |
| B1006-4P-96W | 6 ports network Switch with 4 PoE Ports(Total Power 96W) |
| B1006-4P-135W | 6 ports network Switch with 4 PoE Ports(Total Power 135W) |