B1009-8P+1F-96W

8 RJ-45 10/100M Ports+1 10/100M SFP ports POE Switch with power adapter

Products Description:

The B1009-8P+1F-96W is a 9 ports POE switch with a 100M SFP uplink ports .It provides 8 10/100M RJ45 Ports and 1 100M SFP uplink port and 4/8 PoE ports. The POE ports can automatically detect and supply power for the IEEE802.3af and IEEE802.3at compliant Powered Devices (PDs), like Voip Phone, PoE APs, IP Phones, IP cameras, etc.

The B1009-8P+1F-96W is a small size metal-shell device which is useful for the small office, home and the IP solution project using. All POE ports support both IEEE802.3af and IEEE802.3at Standard; each port can output 30W max. Three optional power supplies for your choice (65W, 96W, 135W, can choose from the order list). Extend Function: Port Lightning protection, Power lightning protection, solid vlan.

Product Features:

- IEEE802.3, IEEE 802.3u, IEEE 802.3ab, IEEE802.3z, IEEE802.3af, IEEE802.3at

- Provides 8 10/100Base-TX ports and 1 10/100M SFP port

- Provides 4 or 8 PoE Port, each port output 30W max power

- Reliable Power Adapter supply power for both network switch and POE

- Three optional power adapters: 65W, 96W, 135W

- 4K entry MAC address table of the PoE switch with auto-learning and auto-aging

- High back-plane bandwidth 1.8Gbps

- IEEE802.3x Flow control for Full-duplex Mode and backpressure for Half-duplex Mode

- Surge protection for power port and data ports

- Compact metal case for desktop or wall-mounting

- EMI standards complies with FCC, CE class B

- Extend Function: Port Lightning protection, Power lightning protection, solid vlan.

Product Specifications:

| Item | Description |
| --- | --- |
| Summarize |
| Fixed port | 8 10/100Base-TX ports. 1 100M SFP ports. |
| POE Port | 8 POE Ports(1-8 Port) or 4 POE ports(1-4 Port) |
| LED Indicators | PWR, PoE, Link/Act LED. |
| Input voltage | 100V～240V AC，50/60Hz (for power adapter) 48VDC (for PoE switch) |
| Network Standard | IEEE 802.3 10Base-T, IEEE 802.3u 100Base-TX, IEEE 802.3x Flow Control, IEEE 802.3az |
| Network Media | 10BASE-TX: UTP category 5, 5e cable (≤250m) 100BASE-TX: UTP category 5, 5e cable (≤150m) Uplink Fiber Port: Single Fiber 20KM, Double Fiber: 20Km |
| Power Supplies | 65W,96W,135W Optional |
| Operating temperature | 0℃～40℃. |
| Storage temperature | -10℃～70℃. |
| Relative humidity | 20%～85% (non-condensing). |
| Thermal methods | Fanless. |
| Switching capacity | 1.8G. |
| MAC address table | 4K. |
| Traffic control | IEEE 802.3x full-duplex flow control. |
| Size | 205*122*33.5cm |
| Weight | <2KG |
| Package | B1009-8P+1F-96W POE switch User Manual Power Adapter Power Cable Warranty Card |
| PoE |
| PoE port | 4/8 10/100Base-TX ports. |
| PoE Standard | IEEE802.3af, IEEE802.3at, per port 15.4W and 30W(MAX), |
| Pin assignment | V+ (RJ45 Pin 1, 2), V- (RJ45 Pin 3, 6). |
| Extend Function | Port Lightning protection, Power lightning protection, solid vlan. |

Order Information

| B1009+8P+1F-65W | 9 ports network Switch with 8 PoE Ports(Total Power 65W) |
| --- | --- |
| B1009+8P+1F-96W | 9 ports network Switch with 8 PoE Ports(Total Power 96W) |
| B1009+8P+1F-135W | 9 ports network Switch with 8 PoE Ports(Total Power 135W) |