B1009-8P-96W

8 RJ-45 10/100M ports POE switch with power adapter(CCTV Mode optional)

Product Description:

The B1009-8P-96W, a low-cost desktop Power-over-Ethernet (POE) switch. It provides 8 10/100Mbps Auto-Negotiation RJ45 ports .The POE ports can automatically detect and supply power for the IEEE802.3af and IEEE802.3at compliant Powered Devices (PDs), like Voip Phone, PoE APs, IP Phones, IP cameras, etc.

The B1009-8P-96W is a small size metal-shell device which is useful for the small office, home and the IP solution project using. All POE ports support both IEEE802.3af and IEEE802.3at Standard; each port can output 30W max. Three optional power supplies for your choice (65W, 96W, 135W, can choose from the order list). Extend Function: Power lightning protection, solid vlan.

- Product Features:

- IEEE802.3, IEEE 802.3u, IEEE 802.3ab, IEEE802.3z, IEEE802.3af, IEEE802.3at

- Provides 8 10/100Base-TX ports

- 8 POE ports, Each POE port output 30W max power

- High back-plane bandwidth 1.6Gbps

- Reliable Power Adapter supply power for both network switch and POE

- Three optional power adapters: 65W, 96W, 135W

- IEEE802.3x Flow control for Full-duplex Mode and backpressure for Half-duplex Mode

- Surge protection for power port and data ports

- Supports IEEE 802.3af and IEEE802.3at compliant Powered Device (PD)

- 2K entry MAC address table of the PoE switch with auto-learning and auto-aging

- Small size metal case for the POE switch

- Pin Feet: V+ (RJ45 Pin 4, 5), V- (RJ45 Pin 7, 8)

- EMI standards complies with FCC, CE class B

- Extend Function: Power lightning protection, solid vlan.

Product Specifications:

| Item | Description |
| --- | --- |
| Summarize |
| Fixed port | 8 10/100Base-TX ports. |
| POE Ports | All 8 POE ports or 4 POE ports( Port 5-8) |
| LED Indicators | PWR, PoE, Link/Act LED. |
| Input voltage | 100V～240V AC，50/60Hz (for power adapter) 48VDC (for switch) |
| Network Media | 10BASE-TX: UTP category 5, 5e cable (≤250m) 100BASE-TX: UTP category 5, 5e cable (≤150m) |
| Forwarding Rate | 10BASE-T: 14880pps/port 100BASE-TX: 148800pps/port |
| Power Supplies | 65W,96W,135W Optional |
| Operating temperature | 0℃～40℃. |
| Storage temperature | -10℃～70℃. |
| Relative humidity | 20%～85% (non-condensing). |
| Thermal methods | Fanless. |
| Switching capacity | 1.6G. |
| MAC address table | 2K. |
| Traffic control | IEEE 802.3x full-duplex flow control. |
| Size | 13.7*7.5*2.5cm |
| Package Size | 19.1*14.1*6.4cm |
| Weight | <2 Kg |
| Package | B1009-8P-96W POE switch User Manual Power Adapter Power Cable Warranty Card |
| PoE |
| PoE port | 4/8 10/100Base-TX ports. |
| PoE Standard | IEEE802.3af, IEEE802.3at, per port 15.4W, max 30W |
| Pin assignment | V+ (RJ45 Pin 4, 5), V- (RJ45 Pin 7, 8). |
| Extend Function | Power lightning protection, solid vlan. |

Order Information

| B1009-8P-65W | 9 ports network Switch with 8 PoE Ports(Total Power 65W) |
| --- | --- |
| B1009-8P-96W | 9 ports network Switch with 8 PoE Ports(Total Power 96W) |
| B1009-8P-135W | 9 ports network Switch with 8 PoE Ports(Total Power 135W) |