BN1018-16P+2C(G)-270W

16+2G Ports Desktop POE Switch with internal power supplies

Product Description:

The BN1018-16P+2C(G)-270W is a 16 ports 10/100M and two Gigabit Uplink Combo Ports desktop POE Switch. It is used for residential building in the corridor-level broadband switching equipment, for the edge of the access and LAN to provide high-quality network connections. It provides 16 10/100Mbps Auto-Negotiation RJ45 ports, 2 Gigabit Combo Ports (SFP+RJ45). The POE ports can automatically detect and supply power for the IEEE802.3af and IEEE802.3at compliant Powered Devices (PDs), like Voip Phone, PoE APs, IP Phones, IP cameras, etc.

The BN1018-16P+2C(G)-270W is a 13’’ case-shaped device with 1U high. It is with the internal industrial power supplies, have two optional power supplies—150W, 270W. All POE ports support both IEEE802.3af and IEEE802.3at Standard; each port can output 30W max.

Product Features:

- IEEE802.3, IEEE 802.3u, IEEE 802.3ab, IEEE802.3z, IEEE802.3af, IEEE802.3at

- Provides 8 10/100Base-TX ports, 2 Gigabit Combo Ports (SFP+RJ45)

- Provides 8 PoE ports, Each POE port output 30W max power

- Build in power supplies, optional 150 or 270W

- High back-plane bandwidth 5.6Gbps

- 4K entry MAC address table of the PoE switch with auto-learning and auto-aging

- IEEE802.3x Flow control

- Surge protection for power port and data ports

- 19’’ rack-mounted size metal case for the POE switch

- Pin Feet: V+ (RJ45 Pin 1, 2), V- (RJ45 Pin 3, 6)

- EMI standards complies with FCC, CE class B

- Extend Function: Power lightning protection, solid vlan.

Product Specifications:

| Item | Description |
| --- | --- |
| Summarize |
| Fixed port | 16 10/100Base-TX ports. 2 Gigabit Combo Ports( SFP+RJ45) |
| LED Indicators | PWR, PoE, Link/Act LED. |
| Input voltage | 100V～240V AC，50/60Hz |
| Network Media | 10BASE-TX: UTP category 5, 5e cable (≤250m) 100BASE-TX: UTP category 5, 5e cable (≤150m) Uplink Fiber Port: Single Fiber 20KM, Double Fiber: 20Km |
| Forwarding Rate | 10BASE-T: 14880pps/port 100BASE-TX: 148800pps/port |
| Power Supplies | 150W, 270W Optional |
| Operating temperature | 0℃～40℃. |
| Storage temperature | -10℃～70℃. |
| Relative humidity | 20%～85% (non-condensing). |
| Thermal methods | Built-in Noiseless FAN. |
| Switching capacity | 5.6G. |
| MAC address table | 4K. |
| Traffic control | IEEE 802.3x full-duplex flow control. |
| Weight | <3 Kg |
| Package | BN1018-16P+2C(G)-270W POE switch User Manual Power Cable Warranty Card |
| PoE |
| PoE port | 16 10/100Base-TX ports. |
| PoE Standard | IEEE802.3af, IEEE802.3at, per port 15.4W, max 30W |
| Pin assignment | V+ (RJ45 Pin 1, 2), V- (RJ45 Pin 3, 6). |

Order Information

| BN1018-16P+2C(G)-150W | 18 ports network Switch with 16 PoE Ports(Total Power 150W) |
| --- | --- |
| BN1018-16P+2C(G)-270W | 18 ports network Switch with 16 PoE Ports(Total Power 270W) |