BN1026-24P+2C(G)-330W

24+2G Ports Desktop POE Switch with internal power supplies

Product Description:

The BN1026-24P+2C(G)-330W is a 24 ports 10/100M and two Gigabit Uplink Combo Ports desktop POE Switch.It is used for residential building in the corridor-level broadband switching equipment, for the edge of the access and LAN to provide high-quality network connections. It provides 24 10/100Mbps Auto-Negotiation RJ45 ports, 2 Gigabit Combo Ports (SFP+RJ45) and 8 POE ports. The POE ports can automatically detect and supply power for the IEEE802.3af and IEEE802.3at compliant Powered Devices (PDs), like Voip Phone, PoE APs, IP Phones, IP cameras, etc.

The BN1026-24P+2C(G)-330W is a 13’’ case-shaped device with 1U high. It is with the internal industrial power supplies, have two optional power supplies—270W,330W. All POE ports support both IEEE802.3af and IEEE802.3at Standard; each port can output 30W max.

Product Features:

- IEEE802.3, IEEE 802.3u, IEEE 802.3ab, IEEE802.3z, IEEE802.3af, IEEE802.3at

- Provides 8 10/100Base-TX ports, 2 Gigabit Combo Ports (SFP+RJ45)

- Provides 8 PoE ports, Each POE port output 30W max power

- Build in power supplies, optional 270W or 330W

- High back-plane bandwidth 5.6Gbps

- 4K entry MAC address table of the PoE switch with auto-learning and auto-aging

- IEEE802.3x Flow control

- Surge protection for power port and data ports

- 19’’ rack-mounted size metal case for the POE switch

- Pin Feet: V+ (RJ45 Pin 1, 2), V- (RJ45 Pin 3, 6)

- EMI standards complies with FCC, CE class B

- Extend Function: Power lightning protection, solid vlan.

Product Specifications:

| Item | Description |
| --- | --- |
| Summarize |
| Fixed port | 24 10/100Base-TX ports. 2 Gigabit Combo Ports( SFP+RJ45) |
| LED Indicators | PWR, PoE, Link/Act LED. |
| Input voltage | 100V～240V AC，50/60Hz |
| Network Media | 10BASE-TX: UTP category 5, 5e cable (≤250m) 100BASE-TX: UTP category 5, 5e cable (≤150m) Uplink Fiber Port: Single Fiber 20KM, Double Fiber: 20Km |
| Forwarding Rate | 10BASE-T: 14880pps/port 100BASE-TX: 148800pps/port |
| Power Supplies | 150W, 270W Optional |
| Operating temperature | 0℃～40℃. |
| Storage temperature | -10℃～70℃. |
| Relative humidity | 20%～85% (non-condensing). |
| Thermal methods | Built-in Noiseless FAN. |
| Switching capacity | 5.6G. |
| MAC address table | 4K. |
| Traffic control | IEEE 802.3x full-duplex flow control. |
| Weight | <3 Kg |
| Package | BN1026-24P+2C(G)-330W POE switch User Manual Power Cable Warranty Card |
| PoE |
| PoE port | 24 10/100Base-TX ports. |
| PoE Standard | IEEE802.3af, IEEE802.3at, per port 15.4W, max 30W |
| Pin assignment | V+ (RJ45 Pin 1, 2), V- (RJ45 Pin 3, 6). |

Order Information

| BN1026-24P+2C(G)-270W | 26 ports network Switch with 24 PoE Ports(Total Power 270W) |
| --- | --- |
| BN1026-24P+2C(G)-330W | 26 ports network Switch with 24 PoE Ports(Total Power 330W) |