BN5026-24P+2C(G)-330W

24+2G Web managed POE Switch with internal power supplies

Product Description:

The BN5026-24P+2C(G)-330W is a 24+2G web-managed POE switch. It provides 24 10/100Mbps Auto-Negotiation RJ45 ports, 2 Gigabit Combo Ports( SFP+RJ45) and 16 or 24 POE ports. The POE ports can automatically detect and supply power for the IEEE802.3af and IEEE802.3at compliant Powered Devices (PDs), like Voip Phone, PoE APs, IP Phones, IP cameras, etc. It have the web-interface firmware to control the network switch function and the POE parts, to the POE parts. The firmware can set POE ON/OFF function based on time and can restart the PD devices if can not signals from them.

The BN5026-24P+2C(G)-330W is a 19’’ case-shaped device with 1U high. It is with the internal industrial power supplies, have three optional power supplies—330W or 450W. All POE ports support both IEEE802.3af and IEEE802.3at Standard; each port can output 30W max. Extend Function: Power lightning protection.

Product Features:

•   IEEE802.3, IEEE 802.3u, IEEE 802.3ab, IEEE802.3z, IEEE802.3af, IEEE802.3at

•   Provides 24 10/100 Base-TX ports, 2 Gigabit Combo Ports (SFP+RJ45)

•   Provides 16/24 PoE ports, Each POE port output 30W max power

•   Build in power supplies, optional 330W or 450W

•   High back-plane bandwidth 8.8Gbps

•   Port mirror and bandwidth control

•   IEEE802.3x Flow control

•   Support Port Based VLAN / 802 .1Q Tag VLAN

•   Support IEEE802.3ad Port trunk with LACP

•   Supports IEEE 802.1p class of service

•   Support Broadcast storm filter

•   Support DHCP client

•   Management by Web

•   Pin Feet: V+ (RJ45 Pin 1, 2), V- (RJ45 Pin 3, 6)

•   Surge protection for power port and data ports

•   EMI standards complies with FCC, CE class B

•   Extend Function: Power lightning protection.

Product Specifications:

| Item | Description |
| --- | --- |
| Summarize |
| Fixed port | 24 10/100Base-TX ports, 2 Gigabit Combo Ports( SFP+RJ45) |
| LED Indicators | PWR, PoE, Link/Act LED. |
| Input voltage | 100V～240V AC，50/60Hz |
| Network Media | 10BASE-TX: UTP category 5, 5e cable (≤250m) 100BASE-TX: UTP category 5, 5e cable (≤150m) Uplink Fiber Port: Single Fiber 20KM, Double Fiber: 20Km |
| Forwarding Rate | 10BASE-T: 14880pps/port 100BASE-TX: 148800pps/port |
| Power Supplies | 330W , 450W Optional |
| Operating temperature | 0℃～40℃. |
| Storage temperature | -10℃～70℃. |
| Relative humidity | 20%～85% (non-condensing). |
| Thermal methods | Built-in Noiseless FAN. |
| PoE |
| PoE port | 16/24 10/100Base-TX ports. |
| PoE Standard | IEEE802.3af, IEEE802.3at |
| Pin assignment | V+ (RJ45 Pin 1, 2), V- (RJ45 Pin 3, 6). |
| Layer 2 Switching |
| Switching capacity | 8.8G |
| MAC address table | 8K. |
| Jumbo Frame | 2K. |
| Port Feature | Port Control. |
| Port Mirroring | Support. |
| VLAN | 4K VLANs. |
| Traffic control | IEEE 802.3x full-duplex flow control. |
| Rate Limit | Unit: 64kbps. |
| Convergence |
| QoS | 4 output queues on each port. Scheduling Method: Strict Priority, Weighted Round Robin. Support port-based classification. |
| Management |
| WEB | Support WEB management system. |
| Configuration File Download/Upload | Support Download/Upload configuration File via WEB. |
| Upgrade Firmware | Support Upgrade Firmware via WEB. |
| Package |
| Unit Size | 44*20*4.4cm |
| Weight | <5KG |
| package | Carton Box |
| Package | BN5026-24P+2C(G)-330W POE Switch User Manual Warranty Card Power Cord*1 Rack Mount Kit*2 Rubber Feet*4 |

Order Information

| BN5026-24P+2C(G)-330W | 26 ports network Switch with 24 PoE Ports(Total Power 330W) |
| --- | --- |
| BN5026-24P+2C(G)-450W | 26 ports network Switch with 24 PoE Ports(Total Power 450W) |