QN1010-8P+2F-150W

8+2SFP Gigabit unmanaged POE Switch with internal power supplies

Product Description:

The QN1010-8P+2F-150W is a 10G unmanaged POE Switch. It provides 8 10/100/100M RJ45 Ports, 2 1000M SFP fiber ports, will be helpful in the security project. It provides 8 PoE ports. The POE ports can automatically detect and supply power for the IEEE802.3af and IEEE802.3at compliant Powered Devices (PDs), like Voip Phone, PoE APs, IP Phones, IP cameras, etc.

The QN1010-8P+2F-150W is a 13’’ case-shaped device with 1U high. It is with the internal industrial power supplies, have two optional power supplies—150W, 270W. All POE ports support both IEEE802.3af and IEEE802.3at Standard; each port can output 30W max. Extend Function: Port Lightning protection, Power lightning protection, solid vlan.

Product Features:

- IEEE802.3, IEEE 802.3u, IEEE 802.3ab, IEEE802.3z, IEEE802.3af, IEEE802.3at

- Provides 8 10/100/1000 Base-TX ports and 2 1000M SFP Ports

- Provides 8 PoE ports, Each POE port output 30W max power

- Build in power supplies, optional 150W or 270W

- High back-plane bandwidth 20Gbps

- Up to 8k MAC address table size

- IEEE802.3x Flow control

- 19’’ rack-mounted size metal case for the POE switch

- Pin Feet: V+ (RJ45 Pin 1, 2), V- (RJ45 Pin 3, 6)

- Surge protection for power port and data ports

- EMI standards complies with FCC, CE class B

- Extend Function: Port Lightning Protection, Power lightning protection, solid vlan.

Product Specifications:

| Item | Description |
| --- | --- |
| Summarize |
| Fixed port | 8 10/100/1000Base-TX ports, 2 1000M SFP ports |
| LED Indicators | PWR, PoE, Link/Act LED. |
| Input voltage | 100V～240V AC，50/60Hz |
| Network Standard | IEEE 802.3 10Base-T, IEEE 802.3u 100Base-TX, IEEE 802.3x Flow Control, IEEE 802.3az |
| Network Media | 10BASE-TX: UTP category 5, 5e cable (≤250m) 100BASE-TX: UTP category 5, 5e cable (≤150m) 1000BASE-TX: UTP category 5, 5e cable (≤150m) Uplink Fiber Port: Single Fiber 20KM, Double Fiber: 20Km |
| Power Supplies | 150W, 270W Optional |
| Operating temperature | 0℃～40℃. |
| Storage temperature | -10℃～70℃. |
| Relative humidity | 20%～85% (non-condensing). |
| Thermal methods | Built-in Noiseless FAN. |
| PoE |
| PoE port | 8 10/100/1000Base-TX ports. |
| PoE Standard | IEEE802.3af, IEEE802.3at, per port 15.4W, MAX 30W. |
| Pin assignment | V+ (RJ45 Pin 1, 2), V- (RJ45 Pin 3, 6). |
| Layer 2 Switching |
| Switching capacity | 20G |
| MAC address table | 8K |
| Weight | <3.5KG |
| Package | QN1010-8P+2F-150W POE switch User Manual Power Cable Warranty Card |

Order Information

| QN1010-8P+2F-150W | 10 ports network Switch with 8 PoE Ports(Total Power 150W) |
| --- | --- |
| QN1010-8P+2F-270W | 10 ports network Switch with 8 PoE Ports(Total Power 270W) |