QN1026-24P+2F-330W

24+2SFP Gigabit POE Switch with internal power supplies

Product Description:

The QN1026-24P+2F-330W is a 26G POE Switch. It provides 24 10/100/100M RJ45 Ports, 2 1000M SFP fiber ports, will be helpful in the security project. It provides 16/24 PoE ports. The POE ports can automatically detect and supply power for the IEEE802.3af and IEEE802.3at compliant Powered Devices (PDs), like Voip Phone, PoE APs, IP Phones, IP cameras, etc.

The QN1026-24P+2F-330W is a 19’’ case-shaped device with 1U high. It is with the internal industrial power supplies, have three optional power supplies—270W, 330W, 500W. All POE ports support both IEEE802.3af and IEEE802.3at Standard; each port can output 30W max.

Product Features:

- IEEE802.3, IEEE 802.3u, IEEE802.3ab, IEEE802.3z, IEEE802.3af, IEEE802.3at

- Provides 24 10/100/1000 Base-TX ports and 2 1000M SFP Ports

- Provides 16/24 PoE ports, Each POE port output 30W max power

- Build in power supplies, optional 270W or 330W or 500W

- High back-plane bandwidth 52Gbps

- Up to 8k MAC address table size

- IEEE802.3x Flow control

- 19’’ rack-mounted size metal case for the POE switch

- Pin Feet: V+ (RJ45 Pin 1, 2), V- (RJ45 Pin 3, 6)

- Surge protection for power port and data ports

- EMI standards complies with FCC, CE class B

Product Specifications:

| Item | Description |
| --- | --- |
| Summarize |
| Fixed port | 24 10/100/1000Base-TX ports, 2 1000M SFP ports |
| LED Indicators | PWR, PoE, Link/Act LED. |
| Input voltage | 100V～240V AC，50/60Hz |
| Network Standard | IEEE 802.3 10Base-T, IEEE 802.3u 100Base-TX, IEEE 802.3x Flow Control, IEEE 802.3az |
| Network Media | 10BASE-TX: UTP category 5, 5e cable (≤250m) 100BASE-TX: UTP category 5, 5e cable (≤150m) 1000BASE-TX: UTP category 5, 5e cable (≤150m) Uplink Fiber Port: Single Fiber 20KM, Double Fiber: 20Km |
| Power Supplies | 270W, 330W，500W Optional |
| Operating temperature | 0℃～40℃. |
| Storage temperature | -10℃～70℃. |
| Relative humidity | 20%～85% (non-condensing). |
| Thermal methods | Built-in Noiseless FAN. |
| PoE |
| PoE port | 16/24 10/100/1000Base-TX ports. |
| PoE Standard | IEEE802.3af, IEEE802.3at, per port 15.4W, MAX 30W. |
| Pin assignment | V+ (RJ45 Pin 1, 2), V- (RJ45 Pin 3, 6). |
| Layer 2 Switching |
| Switching capacity | 52G |
| MAC address table | 8K |
| Weight | <5KG |
| Package | QN1026-24P+2F-330W POE switch User Manual Power Cable Warranty Card |

Order Information

| QN1026-24P+2F-270W | 26 ports network Switch with 24 PoE Ports(Total Power 270W) |
| --- | --- |
| QN1026-24P+2F-330W | 26 ports network Switch with 24 PoE Ports(Total Power 330W) |
| QN1026-24P+2F-500W | 26 ports network Switch with 24 PoE Ports(Total Power 500W) |