QN7012-8P+4F-150W

L2 Managed Gigabit Ethernet Switch

Product Description

The QN7012-8P+4F-270W is a 12G Full Managed POE switch. It provides 8 10/100/1000Mbps Auto-Negotiation RJ45 ports, 4 Gigabit SFP Ports and 8 POE ports. All the POE ports are fit the IEEE802.3af and IEEE802.3at standard. The POE ports can automatically detect and supply power for the IEEE802.3af and IEEE802.3at compliant Powered Devices (PDs), like Voip Phone, PoE APs, IP Phones, IP cameras. This model is designed by Broadcom Chipset and with the managed way by: web, telnet, SNMP and CL (control both network switch and the POE part)

The QN7012-8P+4F-270W is a 13’’ case-shaped device with 1U high. It is with the internal industrial power supplies, have two optional power supplies—150W, 270W. All POE ports support both IEEE802.3af and IEEE802.3at Standard; each port can output 30W max. Extend Function: Power lightning protection.

Product Features:

•	IEEE802.3, IEEE 802.3u, IEEE 802.3ab, IEEE802.3z, IEEE802.3af, IEEE802.3at

•	Provides 8 10/100/1000 Base-TX ports and 4 1000Base-X SFP ports

•   Provides 8 PoE ports, Each POE port output 30W max power

•   Build in power supplies, optional 150W or 270W

•   High back-plane bandwidth 24Gbps

•   Support standard IP/ Extend IP / MAC IP / ARP ACL

•   IGMP snooping and IGMP Query mode for Multi-media application

•   Port mirror and bandwidth control

•   Supports GVRP function

•   IEEE802.3x Flow control

•   Support Port Based VLAN / 802 .1Q Tag VLAN

•   Support IEEE802.3ad Port trunk with LACP

•   Support Spanning tree protocol IEEE 802.1d

•   Supports IEEE 802.1p class of service

•   Support IEEE 802.1x user authentication

•   Support Broadcast storm filter

•   Support DHCP server and client

•   Support System event log

•   Support command line interface management

•   Management by Web/SNMP/Telnet/Console

•   Surge protection for power port and data ports

•   EMI standards complies with FCC, CE class B

Product Specifications:

| Item | Description |
| --- | --- |
| Summarize |
| Fixed port | 8 10/100/1000Base-TX ports. 4 1000Base-X SFP ports. 1 Console port. |
| LED Indicators | PWR, PoE, 1000M and Link/Act LED. |
| Input voltage | 100V～240V AC，50/60Hz |
| Network Media | 10BASE-TX: UTP category 5, 5e cable (≤250m) 100BASE-TX: UTP category 5, 5e cable (≤150m) 1000BASE-TX: UTP category 5, 5e cable (≤150m) Uplink Fiber Port: Single Fiber 20KM, Double Fiber: 20Km |
| Forwarding Rate | 10BASE-T: 14880pps/port 100BASE-TX: 148800pps/port 1000BASE-TX: 148800pps/port |
| Power Supplies | 150W, 270W optional |
| Operating temperature | 0℃～40℃. |
| Storage temperature | -10℃～70℃. |
| Relative humidity | 20%～85% (non-condensing). |
| Thermal methods | Built-in Noiseless FAN. |
| PoE |
| PoE port | 8 10/100/1000Base-TX ports. |
| PoE Standard | IEEE802.3af, IEEE802.3at,per port 15.4W, max 30W |
| Pin assignment | V+ (RJ45 Pin 1, 2), V- (RJ45 Pin 3, 6). |
| PoE management | Support Port-base PoE status view and control. |
| Layer 2 Switching |
| Switching capacity | 24G |
| MAC address table | 8K, Support MAC address table management. |
| MAC Address Binding | Support. |
| MAC Address Filtering | Support. |
| MAC Address Learning control | Control number of port-based MAC address learning. |
| Jumbo Frame | Jumbo packets up to 16379 bytes. |
| Port Feature | Port Control. Port Isolation. Port Self-loop Detection. |
| Port Mirroring | Support. |
| VLAN | 4K 802.1q VLANs, Support Ingress filter. |
| Link Aggregation | Up to 8 maximum aggregation groups, each containing up to 8 GE ports. |
| Traffic control | IEEE 802.3x full-duplex flow control. |
| Rate Limit | Unit: 64kbps. |
| Spanning Tree | IEEE 802.1d Spanning Tree Protocol (STP) IEEE 802.1w Rapid Spanning Tree Protocol (RSTP) IEEE 802.1s Multiple Spanning Tree Protocol (MSTP) |
| Ring Protocol | Support EAPS. |
| Multicast | Support 256 Multicast groups. Support IGMP Snooping. |
| Layer 3 Switching |
| Static ARP | Support. |
| Static Routing | Support. |
| L3 VLAN interface | Up to 32 L3 VLAN Interface. |
| Convergence |
| QoS | 4 output queues on each port. Support flexible queue scheduling algorithms: WRR, Q+WRR. Support port-based / MAC-based / 802.1p / DSCP classification. |
| Security |
| ACL | Support Standard IP / Extend IP / MAC IP / ARP Support 512 entries |
| Security Features | Support MAC-based 802.1X authentication. Support AAA/RADIUS authentication. Support WEB/Telnet password protection. Support Accessing privilege mode password protection. |
| Self-protection | Support CPU Self-protection. |
| Management |
| CLI | Support CLI (Commend Line Interface) configuration mode. |
| Console | Support Configuration via the console port. |
| Telnet | Support Local/remote configuration via Telnet. |
| WEB | Support WEB management system. |
| SNMP | Support System configuration with SNMP v1/v2/v3. |
| User Management | Support Multi-user management. |
| System Log | Support. |
| Configuration File Download/Upload | Support Download/Upload configuration File via WEB/TFTP. |
| Upgrade Firmware | Support Upgrade Firmware via WEB/TFTP/Console. |
| Debug |
| PING | Support. |
| TRACEROUTE | Support. |
| Telnet client | Support. |
| Process View | Support. |
| Package |
| Weight | <4KG |
| package | Carton Box |
| Package | QN7012-8P+4F-270W POE Switch User Manual Warranty Card Power Cord*1 Rack Mount Kit*2 Rubber Feet*4 |

Order Information

| QN7012-8P+4F-150W | 12 ports network Switch with 8 PoE Ports(Total Power 150W) |
| --- | --- |
| QN7012-8P+4F-270W | 12 ports network Switch with 8 PoE Ports(Total Power 270W) |